SEDUM TILE®

Product Specifications

Etera® Green Roof Plants

www.etera.com

SECTION XXXXXX

SEDUM TILE®

GENERAL

SCOPE

Provide all labor, material, tools, and equipment to unload, convey to roof, and install Etera® SEDUM TILE®.

RELATED SECTIONS

Membrane Roofing

Irrigation

QUALITY ASSURANCE

Source Responsibility:  The vegetated roof plant material shall be SEDUM TILE® as provided by Etera®.

Contact:

Etera

sales@etera.com

System Installer:

Company specializing in work of this section with documented experience of comparable scope.

Accepted by Architect as qualified for installing work of this Section prior to Bid Date.

PROJECT CONDITIONS

Environmental Conditions:

SEDUM TILE should not be installed when temperatures are below freezing.

When roof temperatures are expected to reach above100o F (38 o C) on day of installation install tiles early in the day when temperatures are lower, or water the roof growing media to lower the temperature just before installation.

SEDUM TILE should not be installed over waterlogged media.

SEDUM TILE should not be installed during prolonged periods of drought unless irrigation is available.

Existing Conditions:

It is the responsibility of the installer to verify load limits for the roof structure prior to installation of the green roof elements.

It is the responsibility of the installer to inspect or verify inspection of a new or existing roof for watertight conditions prior to installation of the green roof elements.

PRODUCTS

Etera SEDUM TILE:

SEDUM TILE are made up of a coconut fiber base filled with a planting substrate, and pre-cultivated with a layer of low-profile, drought-tolerant vegetation adapted to rooftop conditions.

SEDUM TILE are 12” x 24” (approx. 2.00 sq. ft.) and range from 2” to 4” in height on delivery. (Dependent on the variety of vegetation included.)

SEDUM TILE have a maximum saturated weight of 5.48 lbs per square foot.

SEDUM TILE fiber/soil base – Approximately 1” Thick.

SEDUM TILE shall have a minimum 95% vegetation coverage upon delivery to the site using a succulent plant mix as described below:

1.     Color Max Etera SEDUM TILE – A blend of Sedums for the roof where maximum 	color is desired. This comes in the form of brightly colored foliage, flowers in abundance, 	and colors that blend and go together well. Color Max SEDUM TILE shall consist of   	6 to 8 of the following varieties.  Occasionally substitutes are used.

Sedum acre ‘Aurea’

Sedum album ‘Coral Carpet’

Sedum kamtschaticum ‘Weihenstephaner Gold’

Sedum kamtschaticum ‘Variegatum’

Sedum reflexum ‘Blue Spruce’  Signature Variety

Sedum rupestre ‘Angelina’  Signature Variety

Sedum spurium ‘John Creech’

Sedum spurium ‘Red Carpet’

Tuff Stuff Etera SEDUM TILE – Sometimes particular places are unusually harsh and difficult for plants. The Sedums in Tuff Stuff are the toughest, most durable, most drought-resistant choices available. They have proven ability to survive wind, cold, heat, drought, and tough environments that limit plant choices. Tuff Stuff SEDUM TILE shall consist of 6-8 of the following varieties.  Occasionally substitutes are used.

Sedum album ‘Coral Carpet’

Sedum kamtschaticum

Sedum kamtschaticum ‘Weihenstephaner Gold’

Sedum sexangulare

Sedum takesimensis ‘Golden Carpet’

Sedum spurium ‘Summer Glory’

Sedum spurium ‘Album Superbum’

Sedum spurium ‘Fuldaglut’

IRRIGATION

Irrigation must be applied until the roots are established in the growing media on the roof (4-6 weeks after installation).

Thoroughly water media underneath SEDUM TILE prior to installation and then immediately over SEDUM TILE after installation.

Deliver ≥ ¼” water, 2 x per week for the first 2 weeks, then deliver ≥ ¼” water, 1 x per week for the next 2-4 weeks. Extended irrigation requirements are dependent upon project location, conditions, and plant selection. It is recommended that if a permanent irrigation system is not installed, that a backup system (such as hose bibs located on the roof) be available for use during prolonged periods of drought (>4 weeks with less than a total of ¼” precipitation).

EXECUTION

GENERAL

Etera SEDUM TILE pre-vegetated shall be installed by qualified contractors with demonstrated experience and project references. The tiles shall be installed in such a manner as to not damage or disturb any previously installed roofing components.

DELIVERY, STORAGE, AND HANDLING

SEDUM TILE shall be delivered in such a manner as to preserve the quality of the plants. Truck delivery will be conducted in a manner as to protect the tiles from temperature or wind damage. For transport times less than 1 day, a closed or open trailer may be used. For longer duration transport times, tiles must be delivered in a climate controlled trailer (e.g. refrigerated container).

Upon arrival, the tiles shall be immediately off-loaded and moved to a protected area. Ideally, the tiles are to be installed within 24 hours of arrival.

If installation is not possible in this time frame, then a holding area shall be reserved to store the tiles until they can be installed.

Protect the tiles from weather extremes.

If it is hot, move them to a shady location.

If harsh winter conditions exist, set them out of the wind and protect them from frost.

Store the tiles outside if possible. Tiles can be stored indoors for 1-2 days as long as they are kept cool. Do not store in a closed, hot storage container.

Two day’s storage on the pallet is acceptable while waiting for installation.

If more than two days are needed, the tiles shall be un-stacked and exposed to air and light

Once the tiles are un-stacked, water them thoroughly once every three days until they can be installed.

EXAMINATION

Underlying roof components shall be installed and tested according to manufacturer guidelines.

SEDUM TILE shall be examined for count and any damage that may be present.  Any damage or discrepancy in SEDUM TILE count should be duly noted and photos taken of the damaged material.  Etera shall be notified immediately with a complete description of any damage or missing SEDUM TILE.  Failure to notify Etera within 24 hours of delivery may result in a denial of any claim for damaged or missing SEDUM TILE.

PREPARATION AND INSTALLATION

Growth Media:

SEDUM TILE shall be installed over media specifically engineered for green roofs, preferably to FLL standards.

Spread a minimum of 2-4 (edit to requirements) inches growing media over the green roof system.

Level growing media with a large rake.

Thoroughly wet the media before overlaying with vegetated.

Etera SEDUM TILE:

Install tiles directly over freshly moistened growing media.

Lay tiles smoothly over the growth media, maintaining good overall contact with the media layer and avoiding air gaps between tile and media.

Place tiles close together, avoiding air gaps between them.

The newly installed SEDUM TILE must be immediately and thoroughly watered.

WARRANTY

Etera warrants that our products will conform to the description or pictures presented and will be viable when received. Since we have no control of plant growth once delivered, we give no other warranty, expressed or implied.  Claims will be limited to the amount of the purchase price of the product and any applicable freight and royalty.  Etera will not be held liable for consequential or incidental damages resulting from a shipment, such as:  lost revenue, profit, commission, contamination, legal fees or any other damage

MAINTENANCE

System installer shall maintain the vegetated roof for a period of at least [XXX] (edit to requirements) days from completion.

Maintenance activities shall include:

Water the vegetated roof system twice a week for the first two (2) weeks and once a week for the next 2-4 weeks to aid in root establishment. Water the system more frequently during extended periods of hot, dry weather conditions.

Provide hand weeding as necessary.

Replace areas of damaged plants or dead plants using Sedum plugs or cuttings.

END OF SECTION